## Slide 1: Introduction to Computational Fluid Dynamics (CFD)
Maysam Mousaviraad, Tao Xing, Shanti Bhushan, and Frederick Stern
IIHR—Hydroscience & Engineering
C. Maxwell Stanley Hydraulics Laboratory
The University of Iowa
ENGR:2510 Mechanics of Fluids and Transport Processes
http://css.engineering.uiowa.edu/~fluids/
October 7, 2015

## Slide 2: Outline
1. What, why and where of CFD?
2. Modeling
3. Numerical methods
4. Types of CFD codes
5. ANSYS Interface
6. CFD Process
7. Example of CFD Process
8. 57:020 CFD Labs

## Slide 3: What is CFD?
CFD is the simulation of fluids engineering systems using modeling (mathematical physical problem formulation) and numerical methods (discretization methods, solvers, numerical parameters, and grid generations, etc.)
Historically only Analytical Fluid Dynamics (AFD) and Experimental Fluid Dynamics (EFD).
CFD made possible by the advent of digital computer and advancing with improvements of computer resources
(500 flops, 194720 teraflops, 2003 1.3 pentaflops, Roadrunner at Las Alamos National Lab, 2009.)

## Slide 4: Why use CFD?
Analysis and Design
    1. Simulation-based design instead of “build & test”
      More cost effective and more rapid than EFD
      CFD provides high-fidelity database for diagnosing flow field
    2. Simulation of physical fluid phenomena that are difficult for experiments
      Full scale simulations (e.g., ships and airplanes)
      Environmental effects (wind, weather, etc.)
      Hazards (e.g., explosions, radiation, pollution)
      Physics (e.g., planetary boundary layer, stellar evolution)
Knowledge and exploration of flow physics

## Slide 5: Where is CFD used?
Where is CFD used?
  Aerospace
  Automotive
  Biomedical
  Chemical Processing
  HVAC
  Hydraulics
  Marine
  Oil & Gas
  Power Generation
  Sports
F18 Store Separation
Temperature and natural convection currents in the eye following laser heating.
Aerospace
Automotive
Biomedical

## Slide 6: Where is CFD used?
Polymerization reactor vessel - prediction of flow separation and residence time effects.
Streamlines for workstation ventilation
Where is CFD used?
  Aerospacee
  Automotive
  Biomedical
  Chemical Processing
  HVAC
  Hydraulics
  Marine
  Oil & Gas
  Power Generation
  Sports
HVAC
Chemical Processing
Hydraulics

## Slide 7: Where is CFD used?
Where is CFD used?
  Aerospace
  Automotive
  Biomedical
  Chemical Processing
  HVAC
  Hydraulics
  Marine
  Oil & Gas
  Power Generation
  Sports
Flow of lubricating mud over drill bit
Flow around cooling towers
Marine
Oil & Gas
Sports
Power Generation
http://gallery.ensight.com/keyword/sport/1/701168838_KVnHn#!i=701168838&k=KVnHn

## Slide 8: Modeling
Modeling is the mathematical physics problem formulation in terms of a continuous initial boundary value problem (IBVP)
IBVP is in the form of Partial Differential Equations (PDEs) with appropriate boundary conditions and initial conditions.
Modeling includes:
1. Geometry and domain
2. Coordinates
3. Governing equations
4. Flow conditions
5. Initial and boundary conditions
6. Selection of models for different applications

## Slide 9: Modeling (geometry and domain)
Simple geometries can be easily created by few geometric parameters (e.g. circular pipe)
Complex geometries must be created by the partial differential equations or importing the database of the geometry(e.g. airfoil) into commercial software
Domain: size and shape
Typical approaches
  Geometry approximation
  CAD/CAE integration: use of industry standards such as Parasolid, ACIS, STEP, or IGES, etc.
  The three coordinates: Cartesian system (x,y,z), cylindrical system (r, θ, z), and spherical system(r, θ, Φ) should be appropriately chosen for a better resolution of the geometry (e.g. cylindrical for circular pipe).

## Slide 10: Modeling (coordinates)
x
y
z
x
y
z
x
y
z
(r,,z)
z
r

(r,,)
r


(x,y,z)
Cartesian
Cylindrical
Spherical
General Curvilinear Coordinates
General orthogonal
Coordinates

## Slide 11: Modeling (governing equations)
Navier-Stokes equations (3D in Cartesian coordinates)
Convection
Piezometric pressure gradient
Viscous terms
Local
acceleration
Continuity equation
Equation of state
Rayleigh Equation

## Slide 12: Modeling (flow conditions)
Based on the physics of the fluids phenomena, CFD can be distinguished into different categories using different criteria
  Viscous vs. inviscid (Re)
  External flow or internal flow (wall bounded or not)
  Turbulent vs. laminar (Re)
  Incompressible vs. compressible (Ma)
  Single- vs. multi-phase (Ca)
  Thermal/density effects (Pr, g, Gr, Ec)
  Free-surface flow (Fr) and surface tension (We)
  Chemical reactions and combustion (Pe, Da)
  etc…

## Slide 13: Modeling (initial conditions)
Initial conditions (ICS, steady/unsteady flows)
  ICs should not affect final results and only affect convergence path, i.e. number of iterations (steady) or time steps (unsteady) need to reach converged solutions.
  More reasonable guess can speed up the convergence
  For complicated unsteady flow problems, CFD codes are usually run in the steady mode for a few iterations for getting a better initial conditions

## Slide 14: Modeling(boundary conditions)
Boundary conditions: No-slip or slip-free on walls, periodic, inlet (velocity inlet, mass flow rate, constant pressure, etc.), outlet (constant pressure, velocity convective, numerical beach, zero-gradient), and non-reflecting (for compressible flows, such as acoustics), etc.
No-slip walls: u=0,v=0
v=0, dp/dr=0,du/dr=0
Inlet ,u=c,v=0
Outlet, p=c
Periodic boundary condition in spanwise direction of an airfoil
o
r
x
Axisymmetric

## Slide 15: Modeling (selection of models)
CFD codes typically designed for solving certain fluid
phenomenon by applying different models
  Viscous vs. inviscid (Re)
  Turbulent vs. laminar (Re, Turbulent models)
  Incompressible vs. compressible (Ma, equation of state)
  Single- vs. multi-phase (Ca, cavitation model, two-fluid
  model)
  Thermal/density effects and energy equation
  (Pr, g, Gr, Ec, conservation of energy)
  Free-surface flow (Fr, level-set & surface tracking model) and
  surface tension (We, bubble dynamic model)
  Chemical reactions and combustion (Chemical reaction
  model)
  etc…

## Slide 16: Modeling (Turbulence and free surface models)
Turbulent models:
  DNS: most accurately solve NS equations, but too expensive
  for turbulent flows
  RANS: predict mean flow structures, efficient inside BL but excessive
  diffusion in the separated region.
  LES: accurate in separation region and unaffordable for resolving BL
  DES: RANS inside BL, LES in separated regions.
Free-surface models:
  Surface-tracking method: mesh moving to capture free surface,
  limited to small and medium wave slopes
  Single/two phase level-set method: mesh fixed and level-set
  function used to capture the gas/liquid interface, capable of
  studying steep or breaking waves.
Turbulent flows at high Re usually involve both large and small scale
vortical structures and very thin turbulent boundary layer (BL) near the wall

## Slide 17: Examples of Modeling
Deformation of a sphere.(a)maximum stretching; (b) recovered shape. Left: LS; right: VOF.
Two-phase flow past a surface-piercing cylinder showing vortical structures colored by pressure
Wave breaking in bump flow simulation
Wedge flow simulation
Movie
Movie
Movie

## Slide 18: Numerical methods
The continuous Initial Boundary Value Problems (IBVPs) are discretized into algebraic equations using numerical methods. Assemble the system of algebraic equations and solve the system to get approximate solutions
Numerical methods include:
1. Discretization methods
2. Solvers and numerical parameters
3. Grid generation and transformation
4. High Performance Computation (HPC) and post-
processing

## Slide 19: Discretization methods
Finite difference methods (straightforward to apply, usually for regular grid) and finite volumes and finite element methods (usually for irregular meshes)
Each type of methods above yields the same solution if the grid is fine enough. However, some methods are more suitable to some cases than others
Finite difference methods for spatial derivatives with different order of accuracies can be derived using Taylor expansions, such as 2nd order upwind scheme, central differences schemes, etc.
Higher order numerical methods usually predict higher order of accuracy for CFD, but more likely unstable due to less numerical dissipation
Temporal derivatives can be integrated either by the explicit method (Euler, Runge-Kutta, etc.) or implicit method (e.g. Beam-Warming method)

## Slide 20: Discretization methods (Cont’d)
Explicit methods can be easily applied but yield conditionally stable Finite Different Equations (FDEs), which are restricted by the time step; Implicit methods are unconditionally stable, but need efforts on efficiency.
Usually, higher-order temporal discretization is used when the spatial discretization is also of higher order.
Stability: A discretization method is said to be stable if it does not magnify the errors that appear in the course of numerical solution process.
Pre-conditioning method is used when the matrix of the linear algebraic system is ill-posed, such as multi-phase flows, flows with a broad range of Mach numbers, etc.
Selection of discretization methods should consider efficiency, accuracy and special requirements, such as shock wave tracking.

## Slide 21: Discretization methods (example)
2D incompressible laminar flow boundary layer
m=0
m=1
L-1
L
y
x
m=MM
m=MM+1
(L,m-1)
(L,m)
(L,m+1)
(L-1,m)
FD Sign( )<0
BD Sign( )>0
2nd order central difference
i.e., theoretical order of accuracy
Pkest= 2.
1st order upwind scheme, i.e., theoretical order of accuracy Pkest= 1

## Slide 22: Discretization methods (example)
B2
B3
B1
B4
Solve it using
Thomas algorithm
To be stable, Matrix has to be Diagonally dominant.

## Slide 23: Solvers and numerical parameters
Solvers include: tridiagonal, pentadiagonal solvers, PETSC solver, solution-adaptive solver, multi-grid solvers, etc.
Solvers can be either direct (Cramer’s rule, Gauss elimination, LU decomposition) or iterative (Jacobi method, Gauss-Seidel method, SOR method)
Numerical parameters need to be specified to control the calculation.
  Under relaxation factor, convergence limit, etc.
  Different numerical schemes
  Monitor residuals (change of results between iterations)
  Number of iterations for steady flow or number of time steps for unsteady flow
  Single/double precisions

## Slide 24: Numerical methods (grid generation)
Grids can either be structured (hexahedral) or unstructured (tetrahedral). Depends upon type of discretization scheme and application
  Scheme
    Finite differences: structured
    Finite volume or finite element: structured or unstructured
  Application
    Thin boundary layers best resolved with highly-stretched structured grids
    Unstructured grids useful for complex geometries
    Unstructured grids permit automatic adaptive refinement based on the pressure gradient, or regions interested (FLUENT)
structured
unstructured

## Slide 25: Numerical methods (grid transformation)
y
x
o
o
Physical domain
Computational domain
Transformation between physical (x,y,z) and computational (x,h,z) domains, important for body-fitted grids. The partial derivatives at these two domains have the relationship (2D as an example)
Transform

## Slide 26: High performance computing
CFD computations (e.g. 3D unsteady flows) are usually very expensive which requires parallel high performance supercomputers (e.g. IBM 690) with the use of multi-block technique.
As required by the multi-block technique, CFD codes need to be developed using the Massage Passing Interface (MPI) Standard to transfer data between different blocks.
Emphasis on improving:
  Strong scalability, main bottleneck pressure Poisson solver for incompressible flow.
  Weak scalability, limited by the memory requirements.
Figure: Strong scalability of total times without I/O for CFDShip-Iowa V6 and V4 on NAVO Cray XT5 (Einstein) and IBM P6 (DaVinci) are compared with ideal scaling.
Figure: Weak scalability of total times without I/O for CFDShip-Iowa V6 and V4 on IBM P6 (DaVinci) and SGI Altix (Hawk) are compared with ideal scaling.

## Slide 27
Post-processing: 1. Visualize the CFD results (contour, velocity vectors, streamlines, pathlines, streak lines, and iso-surface in 3D, etc.), and 2. CFD UA: verification and validation using EFD data (more details later)
Post-processing usually through using commercial software
Post-Processing
Figure: Isosurface of Q=300 colored using piezometric pressure, free=surface colored using z for fully appended Athena, Fr=0.25, Re=2.9×108. Tecplot360 is used for visualization.

## Slide 28: Types of CFD codes
Commercial CFD code: FLUENT, Star-CD, CFDRC, CFX/AEA, etc.
Research CFD code: CFDSHIP-IOWA
Public domain software (PHI3D, HYDRO, and WinpipeD, etc.)
Other CFD software includes the Grid generation software (e.g. Gridgen, Gambit) and flow visualization software (e.g. Tecplot, FieldView, EnSight)
CFDSHIPIOWA

## Slide 29: ANSYS Interface
Lab1: Pipe Flow | Lab 2: Airfoil Flow
1. Definition of “CFD Process” 2. Boundary conditions 3. Iterative error 4. Grid error 5. Developing length of laminar and turbulent pipe flows. 6. Verification using AFD 7. Validation using EFD | 1. Boundary conditions 2. Effect of viscous/inviscid simulations 3. Grid generation topology, “C” and “O” Meshes 4. Effect of angle of attack/turbulent models on flow field 5. Validation using EFD

## Slide 30: CFD process
Purposes of CFD codes will be different for different applications: investigation of bubble-fluid interactions for bubbly flows, study of wave induced massively separated flows for free-surface, etc.
Depend on the specific purpose and flow conditions of the problem, different CFD codes can be chosen for different applications (aerospace, marines, combustion, multi-phase flows, etc.)
Once purposes and CFD codes chosen, “CFD process” is the steps to set up the IBVP problem and run the code:
1. Geometry
2. Physics (Setup)
3. Mesh
4. Solution
5. Results

## Slide 31: CFD Process
Viscous Model
(ANSYS Fluent-Setup)
Boundary Conditions
(ANSYS Fluent-Setup)
Initial Conditions
(ANSYS Fluent-Solution)
Convergent Limit
(ANSYS Fluent-Solution)
Contours, Vectors, and Streamlines
(ANSYS Fluent-Results)
Precisions
(ANSYS Fluent-Solution)
Numerical Scheme
(ANSYS Fluent-Solution)
Verification & Validation
(ANSYS Fluent-Results)
Geometry
Geometry Parameters
(ANSYS Design Modeler)
Physics
Mesh
Solution
Flow properties
(ANSYS Fluent-Setup)
Unstructured
(ANSYS Mesh)
Steady/
Unsteady
(ANSYS Fluent-Setup)
Forces Report
(ANSYS Fluent-Results)
XY Plot
(ANSYS Fluent-Results)
Domain Shape and Size
(ANSYS Design Modeler)
Structured
(ANSYS Mesh)
Iterations/
Steps
(ANSYS Fluent-Solution)
Results
Green regions indicate ANSYS modules

## Slide 32: Geometry
Selection of an appropriate coordinate
Determine the domain size and shape
Any simplifications needed?
What kinds of shapes needed to be used to best resolve the geometry? (lines, circular, ovals, etc.)
For commercial code, geometry is usually created using commercial software (either separated from the commercial code itself, like Gambit, or combined together, like ANSYS Design Modeler)
For research code, commercial software (e.g. Gridgen) is used.

## Slide 33: Physics
Flow conditions and fluid properties
1. Flow conditions: inviscid, viscous, laminar, or turbulent, etc.
2. Fluid properties: density, viscosity, and
thermal conductivity, etc.
  3. Flow conditions and properties usually presented in dimensional form in industrial commercial CFD software, whereas in non-dimensional variables for research codes.
Selection of models: different models usually fixed by codes, options for user to choose
Initial and Boundary Conditions: not fixed by codes, user needs specify them for different applications.

## Slide 34: Mesh
Meshes should be well designed to resolve important flow features which are dependent upon flow condition parameters (e.g., Re), such as the grid refinement inside the wall boundary layer
Mesh can be generated by either commercial codes (Gridgen, Gambit, etc.) or research code (using algebraic vs. PDE based, conformal mapping, etc.)
The mesh, together with the boundary conditions need to be exported from commercial software in a certain format that can be recognized by the research CFD code or other commercial CFD software.

## Slide 35: Solution
Setup appropriate numerical parameters
Choose appropriate Solvers
Solution procedure (e.g. incompressible flows)
Solve the momentum, pressure Poisson equations and get flow field quantities, such as velocity, turbulence intensity, pressure and integral quantities (lift, drag forces)

## Slide 36: Results
Time history plots such as the residuals of the velocity, pressure and temperature, etc.
Integral quantities, such as total pressure drop, friction factor (pipe flow), lift and drag coefficients (airfoil flow), etc.
XY plots could present the centerline velocity/pressure distribution, friction factor distribution (pipe flow), pressure coefficient distribution (airfoil flow).
AFD or EFD data can be imported and put on top of the XY plots for validation

## Slide 37: Results
Analysis and visualization
  Calculation of derived variables
    Vorticity
    Wall shear stress
  Calculation of integral parameters: forces, moments
  Visualization (usually with commercial software)
    Simple 2D contours
    3D contour isosurface plots
    Vector plots and streamlines (streamlines are the lines whose tangent direction is the same as the velocity vectors)
    Animations

## Slide 38: Results (Uncertainty Assessment)
Simulation error: the difference between a simulation result S and the truth T (objective reality), assumed composed of additive modeling δSM and numerical δSN errors:
Error: Uncertainty:
Verification: process for assessing simulation numerical uncertainties USN and, when conditions permit, estimating the sign and magnitude Delta δ*SN of the simulation numerical error itself and the uncertainties in that error estimate USN
I: Iterative, G : Grid, T: Time step, P: Input parameters
Validation: process for assessing simulation modeling uncertainty USM by using benchmark experimental data and, when conditions permit, estimating the sign and magnitude of the modeling error δSM itself.
D: EFD Data; UV: Validation Uncertainty
Validation achieved

## Slide 39: Results (UA, Verification)
Convergence studies: Convergence studies require a minimum of m=3 solutions to evaluate convergence with respective to input parameters. Consider the solutions corresponding to fine , medium ,and coarse meshes
(i). Monotonic convergence: 0<Rk<1
(ii). Oscillatory Convergence: Rk<0; | Rk|<1
(iii). Monotonic divergence: Rk>1
(iv). Oscillatory divergence: Rk<0; | Rk|>1
Grid refinement ratio: uniform ratio of grid spacing between meshes.
Monotonic Convergence
Monotonic Divergence
Oscillatory Convergence

## Slide 40: Results (Verification, RE)
Generalized Richardson Extrapolation (RE): For monotonic convergence, generalized RE is used to estimate the error δ*k and order of accuracy pk due to the selection of the kth input parameter.
The error is expanded in a power series expansion with integer powers of xk as a finite sum.
The accuracy of the estimates depends on how many terms are retained in the expansion, the magnitude (importance) of the higher-order terms, and the validity of the assumptions made in RE theory

## Slide 41: Results (Verification, RE)
Power series expansion
Finite sum for the kth parameter and mth solution
order of accuracy for the ith term
Three equations with three unknowns
εSN is the error in the estimate
SC is the numerical benchmark

## Slide 42: Results (UA, Verification, cont’d)
Monotonic Convergence: Generalized Richardson Extrapolation
Oscillatory Convergence: Uncertainties can be estimated, but without
signs and magnitudes of the errors.
Divergence
1. Correction
factors
2. GCI approach
In this course, only grid uncertainties studied. So, all the variables with
subscribe symbol k will be replaced by g, such as “Uk” will be “Ug”
is the theoretical order of accuracy, 2 for 2nd order and 1 for 1st order schemes
is the uncertainties based on fine mesh solution, is the uncertainties based on numerical benchmark SC
is the correction factor
FS: Factor of Safety

## Slide 43: Results (Verification, Asymptotic Range)
Asymptotic Range: For sufficiently small xk, the solutions are in the asymptotic range such that higher-order terms are negligible and the assumption that and are independent of xk is valid.
When Asymptotic Range reached, will be close to the theoretical value , and the correction factor
will be close to 1.
To achieve the asymptotic range for practical geometry and conditions is usually not possible and number of grids m>3 is undesirable from a resources point of view

## Slide 44: Results (UA, Verification, cont’d)
Verification for velocity profile using AFD: To avoid ill-defined ratios, L2 norm of the G21 and G32 are used to define RG and PG
NOTE: For verification using AFD for axial velocity profile in laminar pipe flow (CFD Lab1), there is no modeling error, only grid errors. So, the difference between CFD and AFD, E, can be plot with +Ug and –Ug, and +Ugc and –Ugc to see if solution was verified.
Where <> and || ||2 are used to denote a profile-averaged quantity (with ratio of solution changes based on L2 norms) and L2 norm, respectively.

## Slide 45: Results (Verification: Iterative Convergence)
Typical CFD solution techniques for obtaining steady state solutions involve beginning with an initial guess and performing time marching or iteration until a steady state solution is achieved.
The number of order magnitude drop and final level of solution residual can be used to determine stopping criteria for iterative solution techniques
(1) Oscillatory (2) Convergent (3) Mixed oscillatory/convergent
Iteration history for series 60: (a). Solution change (b) magnified view of total resistance over last two periods of oscillation (Oscillatory iterative convergence)
(b)
(a)

## Slide 46: Results (UA, Validation)
Validation achieved
Validation not achieved
Validation procedure: simulation modeling uncertainties
was presented where for successful validation, the comparison
error, E, is less than the validation uncertainty, Uv.
Interpretation of the results of a validation effort
Validation example
Example: Grid study
and validation of
wave profile for
series 60

## Slide 47: ANSYS Workbench
This project schematic shows the CFD study of airfoil
It includes effect of domain size, domain shape, V&V, effect of angle of attack
Example of CFD Process (Airfoil Simulations)

## Slide 48: ANSYS Design Modeler
Import airfoil geometry and create domain edges
Create surface (‘fluid’)
Split domain
Final Geometry

## Slide 49: ANSYS Mesh
Specify mesh type (structured vs. unstructured etc.)
Edge sizing
Final mesh

## Slide 50: ANSYS Fluent
Boundary conditions
Residuals
Model

## Slide 51: ANSYS Fluent
Analysis of results

## Slide 52: 57:020 CFD Labs
CFD Labs instructed by Michael Conger and Dong-Hwan Kim
Labs held at Seaman’s Center Room#3231 (the AFL Lab)
You can use any computer lab in SC for accessing ANSYS software outside the lab hours
Submit the Prelab Questions at the beginning of the Prelab sessions
CFD office hours will begin Today, Oct. 7.
You need to keep your completed EFD Lab data reduction excel sheets on your H:\ drive or have them with you (in email, USB drive, …) to be used during CFD Labs
Visit class website for more information
http://css.engineering.uiowa.edu/~fluids
CFD Lab | CFD PreLab1 | CFD Lab1 | CFD PreLab2 | CFD Lab 2
Dates | Oct. 13, 15 | Oct. 20, 22 | Nov. 10, 12 | Nov. 17, 19
Schedule