## Slide 1: Numerical Methods in Computational Fluid Dynamics (CFD)
Zhaoyuan Wang, Maysam Mousaviraad, Tao Xing and Fred Stern
IIHR—Hydroscience & Engineering
C. Maxwell Stanley Hydraulics Laboratory
The University of Iowa
ME:5160 Intermediate Mechanics of Fluids
http://css.engineering.uiowa.edu/~me_160/
Oct. 11, 2019

## Slide 2: Outline
Introduction to Numerical Methods
Components of Numerical Methods
2.1. Properties of Numerical Methods
2.2. Discretization Methods
2.3. Application of Numerical methods in PDE
2.4. Numerical Grid and Coordinates
2.5. Solution of Linear Equation System
2.6. Convergence Criteria
Methods for Unsteady Problems
Solution of Navier-Stokes Equations
Example

## Slide 3: Introduction to numerical methods
Approaches to Fluid Dynamical Problems:
1. Simplifications of the governing equations AFD
2. Experiments on scale models EFD
3. Discretize governing equations and solve by computers CFD
CFD is the simulation of fluids engineering system using modeling and numerical methods
Possibilities and Limitations of Numerical Methods:
1. Coding level: quality assurance, programming
defects, inappropriate algorithm, etc.
2. Simulation level: iterative error, truncation error, grid
error, etc.

## Slide 4: Components of numerical methods (Properties)
Consistence
1. The discretization should become exact as the grid spacing
tends to zero
2. Truncation error: Difference between the discretized equation
and the exact one
Stability: does not magnify the errors that appear in the course of numerical solution process.
1. Iterative methods: not diverge
2. Temporal problems: bounded solutions
3. Von Neumann’s method
4. Difficulty due to boundary conditions and non-linearities
present.
Convergence: solution of the discretized equations tends to the exact solution of the differential equation as the grid spacing tends to zero.

## Slide 5: Components of numerical methods (Properties, Cont’d)
Conservation
1. The numerical scheme should on both local and global basis respect the conservation laws.
2. Automatically satisfied for control volume method, either individual control volume or the whole domain.
3. Errors due to non-conservation are in most cases appreciable only on relatively coarse grids, but hard to estimate quantitatively
Boundedness:
1. Numerical solutions should lie within proper bounds (e.g. non-negative density and TKE for turbulence; concentration between 0% and 100%, VOF between 0 and 1, etc.)
2. Difficult to guarantee, especially for higher order schemes.
Realizability: models of phenomena which are too complex to treat directly (turbulence, combustion, or multiphase flow) should be designed to guarantee physically realistic solutions.
Accuracy: 1. Modeling error 2. Discretization errors 3. Iterative errors

## Slide 6: Components of numerical methods (Discretization Methods)
Finite Difference Method (focused in this lecture)
1. Introduced by Euler in the 18th century.
2. Governing equations in differential form domain with grid replacing the partial derivatives by approximations in terms of node values of the functions one algebraic equation per grid node linear algebraic equation system.
3. Applied to structured grids
Finite Volume Method (not focused in this lecture)
1. Governing equations in integral form solution domain is subdivided into a finite number of contiguous control volumes conservation equation applied to each CV.
2. Computational node locates at the centroid of each CV.
3. Applied to any type of grids, especially complex geometries
4. Compared to FD, FV with methods higher than 2nd order will be difficult, especially for 3D. Good mass conservation.
Finite Element Method (not covered in this lecture):
1. Similar to FV
2. Equations are multiplied by a weight function before integrated over the entire domain. Often used for Solid Mechanics.

## Slide 7: Discretization methods (Finite Difference, introduction)
First step in obtaining a numerical solution is to discretize the geometric domain to define a numerical grid
Each node has one unknown and need one algebraic equation, which is a relation between the variable value at that node and those at some of the neighboring nodes.
The approach is to replace each term of the PDE at the particular node by a finite-difference approximation.
Numbers of equations and unknowns must be equal

## Slide 8: Discretization methods (Finite Difference, approximation of the first derivative)
Taylor Series Expansion: Any continuous differentiable function, in the vicinity of xi , can be expressed as a Taylor series:
Higher order derivatives are unknown and can be dropped when the distance between grid points is small.
By writing Taylor series at different nodes, xi-1, xi+1, or both xi-1 and xi+1, we can have:
Forward-FDS
(forward difference scheme)
Backward-BDS
Central-CDS
1st order, order of accuracy Pkest=1
2nd order, order of accuracy Pkest=2

## Slide 9: Discretization methods (Finite Difference, approximation of the first derivative, Cont’d)
Polynomial fitting: fit the function to an interpolation curve and differentiate the resulting curve.
Example: fitting a parabola to the data at points xi-1,xi, and xi+1, and computing the first derivative at xi, we obtain:
Compact schemes: Depending on the choice of parameters α, β, and γ, 2nd order and 4th order CDS, 4th order and 6th order Pade scheme are obtained.
2nd order truncation error on any grid. For uniform meshing, it reduced to the CDS approximation given in previous slide.
Non-Uniform Grids: to spread the error nearly uniformly over the domain, it will be necessary to use smaller x in regions where derivatives of the function are large and larger x where function is smooth. Save computational resources.

## Slide 10: Discretization methods (Finite Difference, approximation of the second derivative)
Geometrically, the second derivative is the slope of the line tangent to the curve representing the first derivative.
Estimate the outer derivative by FDS, and estimate the inner derivatives using BDS, we get
For equidistant spacing of the points:
Higher-order approximations for the second derivative can be
derived by including more data points, such as xi-2, and xi+2, even
xi-3, and xi+3

## Slide 11: Discretization methods (Finite Volume)
W
P
WW
E
EE
N
Typical CV and the notation for Cartesian 2D
n
ne
nw
se
sw
e
w
s
x
y
ne
NW
NE
SW
SE
x
y
i
j
FV defines the control volume boundaries while FD define the computational nodes
Computational node located at the Control Volume center
Global conservation automatically satisfied
FV methods uses the integral form of the conservation equation
FV methods use the integral form of the conservation equation

## Slide 12: Application of numerical methods in PDE
Fluid Mechanics problems are governed by the laws of physics, which are formulated for unsteady flows as initial and boundary value problems (IBVP), which is defined by a continuous partial differential equation (PDE) operator LT (no modeling or numerical errors, T is the true or exact solution)
Analytical and CFD approaches formulate the IBVP by selection of the PDE, IC, and BC to model the physical phenomena
Using numerical methods, the continuous IBVP is reduced to a discrete IBVP (computer code), and thus introduce numerical errors:
Numerical errors can be defined and evaluated by transforming the discrete IBVP back to a continuous IBVP.
Truncation error
A1
A2
A3
A4

## Slide 13: Application of numerical methods in PDE (Truncation and Discretization errors)
Subtracting equations A2 and A4 gives the IBVP that governs the simulation numerical error
An IBVP for the modeling error M-T can be obtained by subtracting A1 and A2:
A5
A6
Adding A5 and A6

## Slide 14: Numerical grids and coordinates
The discrete locations at which the variables are to be calculated are defined by the numerical grid
Numerical grid is a discrete representation of the geometric domain on which the problem is to be solved. It divides the solution domain into a finite number of sub-domains
Type of numerical grids: 1. structured (regular grid), 2. Block-structured grids, and
3. Unstructured grids
Detailed explanations of numerical grids will be presented in the last lecture of this CFD lecture series.
Different coordinates have been covered in “Introduction to CFD”

## Slide 15: Components of numerical methods (Solution of linear equation systems, introduction)
The result of the discretization using either FD or FV, is a system of algebraic equations, which are linear or non-linear
For non-linear case, the system must be solved using iterative methods, i.e. initial guess iterate converged results obtained.
The matrices derived from partial differential equations are always sparse with the non-zero elements of the matrices lie on a small number of well-defined diagonals

## Slide 16: Solution of linear equation systems (direct methods)
Gauss Elimination: Basic methods for solving linear systems of algebraic equations but does not vectorize or parallelize well and is rarely used without modifications in CFD problems.
LU Decomposition: the factorization can be performed without knowing the vector Q
Tridiagonal Systems: Thomas Algorithm or Tridiagonal Matrix Algorithm (TDMA) P95

## Slide 17: Solution of linear equation systems (iterative methods)
Why use iterative methods:
1. in CFD, the cost of direct methods is too high since the
triangular factors of sparse matrices are not sparse.
2. Discretization error is larger than the accuracy of the
computer arithmetic
Purpose of iteration methods: drive both the residual and iterative error to be zero
Rapid convergence of an iterative method is key to its effectiveness.
Approximate solution after n iteration
residual
Iteration error

## Slide 18: Solution of linear equation systems (iterative methods, cont’d)
Typical iterative methods:
1. Jacobi method
2. Gauss-Seidel method
3. Successive Over-Relaxation (SOR), or LSOR
4. Alternative Direction Implicit (ADI) method
5. Conjugate Gradient Methods
6. Biconjugate Gradients and CGSTAB
7. Multigrid Methods

## Slide 19: Solution of linear equation systems (iterative methods, examples)
Jacobi method:
Gauss-Seidel method: similar to Jacobi method, but most recently computed values of all are used in all computations.
Successive Overrelaxation (SOR):

## Slide 20: Solution of linear equation systems (coupled equations and their solutions)
Definition: Most problems in fluid dynamics require solution of coupled systems of equations, i.e. dominant variable of each equation occurs in some of the other equations
Solution approaches:
1. Simultaneous solution: all variables are solved for
simultaneously
2. Sequential Solution: Each equation is solved for
its dominant variable, treating the other variables
as known, and iterating until the solution is
obtained.
For sequential solution, inner iterations and outer iterations are necessary

## Slide 21: Solution of linear equation systems (non-linear equations and their solutions)
Definition:
Given the continuous nonlinear function f(x), find the value x=α, such that f(α)=0 or f(α)=β
Solution approaches:
1. Newton-like Techniques: root finding algorithm, faster but need good estimation of the solution. Seldom used for solving Navier-Stokes equations.
2. Global: guarantee not to diverge but slower, such as sequential decoupled method

## Slide 22: Solution of linear equation systems (convergence criteria and iteration errors)
Convergence Criteria: Used to determine when to quit for iteration method
1. Difference between two successive iterates
2. Order drops of the residuals
3. Integral variable vs. iteration history
Inner iterations can be stopped when the residual has fallen by one to two orders of magnitude.
Details on how to estimate iterative errors have been presented in CFD lecture.
(for all i, j)
(for all i, j)

## Slide 23: Methods for unsteady problems (introduction)
Unsteady flows have a fourth coordinate direction– time, which must be discretized.
Differences with spatial discretization: a force at any space location may influence the flow anywhere else, forcing at a given instant will affect the flow only in the future (parabolic like).
These methods are very similar to ones applied to initial value problems for ordinary differential equations.
The basic problem is to find the solution a short
time t after the initial point. The solution at t1=t0+ t,
can be used as a new initial condition and the solution
can be advanced to t2=t1+ t , t3=t2+ t, ….etc.

## Slide 24: Methods for unsteady problems
Methods for Initial Value Problems in ODEs
1. Two-Level Methods (explicit/implicit Euler)
2. Predictor-Corrector and Multipoint Methods
3. Runge-Kutta Methods
4. Other methods: Lagrangian and Semi-Lagrangian scheme
Application to the Generic Transport Equation
1. Explicit methods
2. Implicit methods
3. Other methods

## Slide 25: Methods for unsteady problems (examples)
Methods for Initial Value Problems in ODEs (4th order Runge-Kutta method)
Methods for Initial Value Problems in ODEs (explicit and implicit Euler method)
explicit
implicit

## Slide 26: Methods for unsteady problems (examples)
Application to the Generic Transport Equation
(Explicit Euler methods)
Assume constant velocity
Courant number (or CFL number) when diffusion negligible, Courant number should be smaller than unity to make the scheme stable
Time required for a disturbance to be transmitted
By diffusion over a distance x

## Slide 27: Methods for unsteady problems (examples)
Application to the Generic Transport Equation
(Implicit Euler methods)
Assume constant velocity
Advantage: Use of the implicit Euler method allows arbitrarily large time steps to be taken
Disadvantage: first order truncation error in time and the need to solve a large coupled set of equations at each time step, and more computational time for iterations.

## Slide 28: Solution of Navier-Stokes equations
Special features of Navier-Stokes Equations
Choice of Variable Arrangement on the Grid
Pressure Poisson equation
Solution methods for N-S equations

## Slide 29: Solution of N-S equations (special features)
Navier-Stokes equations (3D in Cartesian coordinates)
Convection
Piezometric pressure gradient
Viscous terms
Local
acceleration
Continuity equation
Discretization of Convective, pressure and Viscous terms
Conservation properties: 1. Guaranteeing global energy conservation in a numerical method is a worthwhile goal, but not easily attained;
2. Incompressible isothermal flows, significance is kinetic energy; 3. heat transfer: thermal energy>>kinetic energy

## Slide 30: Solution of N-S equations (choice of variable arrangement on the grid)
Collocated arrangement:
1. Store all the variables at the same set of grid points and to use the
same control volume for all variables
2. Advantages: easy to code
3. Disadvantages: pressure-velocity decoupling, approximation for terms
Staggered Arrangements:
1. Not all variables share the same grid
2. Advantages: (1). Strong coupling between pressure and velocities, (2). Some terms interpolation in collocated arrangement can be calculated with interpolation.
3. Disadvantages: higher order numerical schemes with order higher than 2nd will be difficult
Colocated
Staggered

## Slide 31: Solution of Navier-Stokes equations (Pressure Poisson equation)
Why need equation for pressure: 1. N-S equations lack an independent equation for the pressure; 2. in incompressible flows, continuity equation cannot be used directly
Derivation: obtain Poisson equation by taking the divergence of the momentum equation and then simplify using the continuity equation.
Poisson equation is an elliptic problem, i.e. pressure values on boundaries must be known to compute the whole flow field

## Slide 32: Solution methods for the Navier-Stokes equations
Analytical Solution (fully developed laminar pipe flow)
Vorticity-Stream Function Approach: eliminate pressure term
The SIMPLE (Semi-Implicit Method for pressure-Linked Equations) Algorithm:
1. Guess the pressure field p*
2. Solve the momentum equations to obtain u*,v*,w*
3. Solve the p’ equation (The pressure-correction equation)
4. p=p*+p’
5. Calculate u, v, w from their starred values using the
velocity-correction equations
6. Solve the discretization equation for other variables, such as
temperature, concentration, and turbulence quantities.
7. Treat the corrected pressure p as a new guessed pressure p*,
return to step 2, and repeat the whole procedure until a
converged solution is obtained.

## Slide 33: Example (lid-driven cavity)
The driven cavity problem is a classical problem that has wall boundaries surrounding the entire computational region.
Incompressible viscous flow in the cavity is driven by the uniform translation of the moving upper lid.
the vorticity-stream function method is used to solve the driven cavity problem.
UTOP
o
y
x
u=v=0
u=v=0
u=v=0
u=UTOP, v=0

## Slide 34: Example (lid-driven cavity, governing equations)

## Slide 35: Example (lid-driven cavity, boundary conditions)
on all walls
The other
Three walls
The top wall
For wall pressures, using the tangential momentum equation to the fluid adjacent to the wall surface, get:
* s is measured along the wall surface and n is normal to it
* Pressure at the lower left corner of the cavity is assigned 1.0

## Slide 36: Example (lid-driven cavity, discretization methods)
2nd order central difference scheme used for all spatial derivatives
1st order upwind for
time derivative

## Slide 37: Example (lid-driven cavity, solution procedure)
Specify the geometry and fluid properties
Specify initial conditions (e.g. u=v= = =0).
Specify boundary conditions
Determine t
Solve the vorticity transport equation for
Solve stream function equation for
Solve for un+1 and vn+1
Solve the boundary conditions for on the walls
Continue marching to time of interest, or until the steady state is reached.

## Slide 38: Example (lid-driven cavity, residuals)
and

## Slide 39: Example (lid-driven cavity, sample results)

## Slide 40: Some good books
J. H. Ferziger, M. Peric, “ Computational Methods for Fluid
Dynamics,” 3rd edition, Springer, 2002.
Patric J. Roache, “Verification and Validation in
Computational Science and Engineering,” Hermosa
publishers, 1998
Frank, M. White, “Viscous Fluid Flow,” 3rd edition,
McGraw-Hill Inc., 2006