## Slide 1: ME: 7268 Turbulent Flows Class Project
February 27, 2025

## Slide 2: Velocity Statistic Analysis
U(t), V(t), and W(t) time series provided (filtered and unfiltered)
Extract fluctuating component:
  Python (with NumPy):
    = np.mean(U(t), axis=a) or mean = x.mean(axis=a)
      Confirm that axis “a” should correspond to the axis in the time direction of your array
  MATLAB
    = mean(U(t),dim)
      Confirm that dim should correspond to axis in the time direction
  u(t) = U(t) - (and similarly for v and w)
Use u(t), v(t), and w(t) to get Reynolds Stresses and TKE
  (scalar value for each dataset)
  Python/NumPy
    np.mean(u(t)*v(t)) (* operator is equivalent to np.multiply which is element-wise)
  MATLAB
    mean(u(t) .* v(t))
  tke = ½( + + )
Ensemble average the Reynolds stresses and mean U(t) velocity from each dataset / experimental trial

## Slide 3: Autocorrelations
Python
  SciPy or statsmodels libraries would be good choice
    correlate() or acf() function names
    Both have “direct” or “fft” method options
    Both only return the resulting correlation function (need to compute the time lag vector)
MATLAB
  autocorr()
  Will return correlation function and lags
acf (python) and autocorr (MATLAB) also allow you specify number of lags to use
  Use length of time series for the nlags argument

## Slide 4: Autocorrelation (cont.)
RE
t
Autocorrelation Functions of SDVP vortex core at x/L = 0.12
Ensemble the autocorrelation functions together
  Use np.mean (Python) or mean (MATLAB) functions
  adjust axis or dim argument appropriately
Use first 2* points to fit a parabola
  “mirror” the point at t1 across y-axis
  Use points at t-1 , t0 , t1 with:
    np.polyfit (python)
    polyfit (MATLAB)
    Use n = 2 (second order polynomial)
  Both function will return coefficients for a parabola
Use coefficients to plot the parabolic fit and determine tE (Taylor micro scale)
  Can use “roots” function from NumPy or MATLAB or use Eqn. from instructions with 2nd derivative of RE (should be equivalent)

## Slide 5: Autocorrelation (cont.)
Determine the zero-crossing (ZC) point of the RE
  Integrate RE from 0 to ZC point to determine T (Taylor macro scale)
  SciPy and MATLAB should have functions you can use to do this
    Trapezoidal or Simpson’s rule numerical integration methods recommended
      Not sure MATLAB has a built-in Simpson’s rule integration function
Convert T and tE from time scales to length scales with Taylor’s frozen turbulence hypothesis (TFTH)
  Use ensembled mean velocity from earlier statistics analysis

## Slide 6: Report macro and micro scales
Use the current results to report ensemble averaged macro and micro scale parameters
  Note that there is a macro scale estimate for e and a micro scale estimate for e
Macro scales to report:
  Use equations from instructions
  , , u0, u’, l0, e, and Rel0
Micro scales to report:
  Use equations in instructions
  lf, Lf, e, and h
It is a good idea for your code to output your data to a delimted or excel file
  You can write to a delimited file by hand
  Otherwise:
    In Python: the Pandas library can write to an excel or CSV file for you
    In MATLAB: the writetable() function can write your output to excel or CSV

## Slide 7: 1D Energy Spectrum
MATLAB and SciPy have fft functions that can be used to get E11 spectrum in the frequency domain
  You can take FFT of RE or using the power spectral density (PSD)/convolution approach on u(t)
  Both methods are given in the instructions
  Windowing functions may need to be used (more details to come)
However, we likely will provide you with an fft function to use to ensure consistency and proper scaling of the output between everyone’s results

## Slide 8: Analyzing E11
First, convert E11 from the frequency domain wavenumber space (k1) with TFTH as per instructions:
Plot (and save) E11 spectra for unscaled (freq. domain, wavenumber domain), Kolmogorov scaling, and compensated scaling (using both log-linear and linear-log axes)
  Scaling are included in the instructions