## Slide 1
55:148 Digital Image Processing
Chapter 11 3D Vision, Geometry
Topics:
  Basics of projective geometry
    Points and hyperplanes in projective space
    Homography
    Estimating homography from point correspondence
  The single perspective camera
    An overview of single camera calibration
    Calibration of one camera from the known scene
  Scene reconstruction from multiple views
  Triangulation
  Projective reconstruction
  Matching constraints
  Bundle adjustment
  Two cameras, stereopsis
    The geometry of two cameras. The fundamental matrix
    Relative motion of the camera; the essential matrix
    Estimation of a fundamental matrix from image point correspondences
    Camera Image rectification
    Applications of the epipolar geometry in vision
  Three and more cameras
    Stereo correspondence algorithms

## Slide 2
Epipolar geometry and Fundamental matrix
Fundamental matrix relates corresponding points in two stereo images
What does it mean?
A point on the left image ≈ a line on the right image
What is this line called

## Slide 3
Fundamental matrices relating multiple cameras

## Slide 4
Fundamental matrices relating multiple cameras

## Slide 5
Fundamental matrices relating multiple cameras

## Slide 6
Fundamental matrices relating multiple cameras

## Slide 7
Image rectification (before)

## Slide 8
Image rectification (after)

## Slide 9
Image rectification
What happens in terms of epipolar geometry?
Where are the two epipoles?
What is the relation between the baseline and the camera matrix?
Can we solve it using a homographic transformation on each camera image?

## Slide 10
Image rectification
What happens in terms of epipolar geometry?
Where are the two epipoles?
What is the relation between the baseline and the camera matrix?
Can we solve it using a homographic transformation on each camera image?

## Slide 11
Image rectification: advantages
3D reconstruction becomes easier
Image stitching to generate a panoramic view
a
b
c

## Slide 12
Panoramic view

## Slide 13
So, how to accomplish image rectification?
Learn how to determine the fundamental matrix
Relative camera motion and essential matrix
Relation between fundamental matrix and camera matrix
Compute image rectification

## Slide 14
Relative camera motion and essential matrix
In the previous class, we have seen:
and are intrinsic camera parameters that maps Euclidean image plane to image pixels; primarily plays a role to correct the shear distortion between the x- and y-axes.
It’s very difficult to determine and without use of a known 3D scene and just by using the correspondence between two acquired images
Thus, if we ignore this shear component, the epipolar constraint in the image Euclidean plane translates to
is called the essential matrix that defines the relative motion between two camera position
Application: Determine camera movements from a video image (http://www.2d3.com/)
Relation between fundamental matrix and essential matrix (when we know and )

## Slide 15
Decomposition of essential matrix
Note that the vector in the essential matrix tells us about the relative location of the two optical centers. i.e., the baseline.
Also, assuming that the camera matrix for the first camera, and together determine -- the camera matrix of the second camera
Now, assume that, somehow, we have computed the essential matrix
But, it does not immediately give us the translation vector or the rotation matrix
So, we need to decompose
Singular value decomposition of gives , and are rotation matrices.
Following that the rows of are coplanar (why), it has a rank of two and the two singular values are equal (follows from the formulation of ); so
We will later see that scale factor in the actual computation of is arbitrarily set

## Slide 16
Decomposition of the essential matrix continued …
Denote
Then the translation vector is given by
The rotation matrix is not given uniquely, we have

## Slide 17
Before getting into image rectification, we need to learn
Relation between the fundamental matrix and the camera matrix
How to compute the fundamental matrix
Camera matrices:

## Slide 18
Computation of the fundamental matrix using point correspondence
Number of unknowns:
9 parameters in minus one for scale standardization minus one for rank of is two
So, we can solve with corresponding point pairs in two images.
We have to solve the following linear system:
Use Kronecker product identity:
Put together all point correspondences
Compute and apply singular value decomposition; choose along the eigenvector corresponding to the smallest eigenvalue

## Slide 19
Computation of the fundamental matrix using maximum likelihood estimation
Given and
Use Lagrange multiplier
, given
is equivalent to optimizing the Lagrange function
where is the new variable called Lagrange multiplier