## Slide 1
55:148 Digital Image Processing
Chapter 11 3D Vision, Geometry
Topics:
  Basics of projective geometry
    Points and hyperplanes in projective space
    Homography
    Estimating homography from point correspondence
  The single perspective camera
    An overview of single camera calibration
    Calibration of one camera from the known scene
  Two cameras, stereopsis
    The geometry of two cameras. The fundamental matrix
    Relative motion of the camera; the essential matrix
    Estimation of a fundamental matrix from image point correspondences
    Applications of the epipolar geometry in vision
  Three and more cameras
    Stereo correspondence algorithms
Green = To be discussed today

## Slide 2
Kronecker product
In mathematics, the Kronecker product, denoted by “”, is an operation on two matrices of arbitrary size resulting in a block matrix. The Kronecker product should NOT be confused with the usual matrix multiplication, which is an entirely different operation.
If is an -by- matrix and is a -by- matrix, then the Kronecker product is the -by- block matrix
Example
We will use the following identity

## Slide 3
Linear estimation
Why linear estimation?
Cost function for maximum likelihood estimation
Maximum likelihood estimation: non convex cost function → multiple optimal solutions (local optimal problem) → a need for initial estimation of the matrix
Linear estimation approach is used to solve the initialization problem

## Slide 4
Linear estimation
Principle: minimize the sum of algebraic distance between the estimated (transformed from first projection) and actual points in the second position
Advantage: canonical solution, i.e., no optimization search algorithm is needed → unique optimum
Method:
Start with the equation
Eliminate the term by multiplying with a matrix whose rows are orthogonal to and ; example:
Rearrange the equation using the identity of Kronecker product identity
where

## Slide 5
Linear estimation Method
Combine correspondences into a single matrix form
In real application this equality does not hold good (why??); so, it boils down to a minimization of the term on the l.h.s., i.e., subject to
Soln: Compute square matrix
  Compute eigenvectors and eigenvalues of
  Find along the eigenvector associated with the smallest eigenvalue
Data preconditioning:
  Use and to pre the data points such mean and std of points on each project are 0 and 1, respectively
Finally,

## Slide 6
11.3 A single projection camera
11.3.1 Camera model
Different coordinate system
Transformation between every two coordinate systems
Homogeneous coordinates
Image points:
3D scene points:
In a homogeneous coordinate, the last element or W is used to indicate the ‘’ parameter of Eq. 11.1. Thus a homogeneous coordinate represents a ray.
All points with lie on the image plane.
Thus, by performing all transformations on homogeneous coordinates, we do not only transform a set of points onto another set of points; rather, a set of rays is transformed onto another set of rays.

## Slide 7
Camera model
Important parameters
Image plane
Optical axis
Focal point/optical center/center of projection
Different coordinate systems
World/scene coordinate system
Camera coordinate system
Image Euclidean coordinate system
Image affine coordinate system

## Slide 8
Transformations between different coordinate systems
Scene → Camera
Non-homogeneous coordinates
Homogeneous coordinates
and are called extrinsic camera calibration parameters

## Slide 9
Camera→ Image Euclidean
Non-homogeneous coordinates
Homogeneous coordinates
Explain the relation between the above two equations
Normalized image plane ()

## Slide 10
Image Euclidean → Image affine
Homogeneous coordinates
Explain different parameters in the matrix
is called the intrinsic calibration matrix
Note that represents the image pixel coordinate system

## Slide 11
Scene → Image affine
Homogeneous coordinates
is called the projection matrix

## Slide 12
Projection and back projection
Here, homogeneous coordinates are used
To compute the inverse map we need to compute the inverse of
But is not a square matrix!
How to solve it?
Use pseudo inverse ; Property
Image → Scene transformation
Does it mean that we can uniquely map a 2D image point to a 3D scene point?

## Slide 13
Projection and back projection
Here, homogeneous coordinates are used
To compute the inverse map we need to compute the inverse of
But is not a square matrix!
How to solve it?
Use pseudo inverse ; Property
Image → Scene transformation
Does it mean that we can uniquely map a 2D image point to a 3D scene point? NO!
Note that we are using homogeneous coordinate which represent a ray and not a point
So the above equation maps a ray from the image affine coordinate system to scene coordinate system
Here is the beauty of homogenous coordinate system; it does not solve the ambiguity but provide a compact mathematical representation in the presence of ambiguity

## Slide 14
Back projection of an image line
Given: an image line
Note that, in homogeneous coordinates, a image line represents a plane, say
A scene point on the plane satisfies
Now, the projection of , say , must lie on the line
Thus,
The plane contains the optical center, i.e, .

## Slide 15
11.3.3 Camera calibration from a known scene
We want to derive the projection matrix that consists of both extrinsic camera calibration parameters (what are those?) and the intrinsic calibration matrix (again, what is that?)
Given: a set of image-scene point correspondences
Output: the projection matrix
It sounds like we have solved a similar problem before!!

## Slide 16
11.3.3 Camera calibration from a known scene
We want to derive the projection matrix that consists of both extrinsic camera calibration parameters (what are those?) and the intrinsic calibration matrix (again, what is that?)
Given: a set of image-scene point correspondences
Output: the projection matrix
It sounds like we have solved a similar problem before!!
Remember the process of homography estimation
What is the comparison?

## Slide 17
11.3.3 Camera calibration from a known scene
We want to derive the projection matrix that consists of both extrinsic camera calibration parameters (what are those?) and the intrinsic calibration matrix (again, what is that?)
Given: a set of image-scene point correspondences
Output: the projection matrix
It sounds like we have solved a similar problem before!!
Remember the process of homography estimation
What is the comparison?
In homography estimation we solved a matrix using a correspondence
Here we have to solve a matrix using a correspondence
Remember that we are using homogeneous coordinates
Steps?

## Slide 18
11.3.3 Camera calibration from a known scene
We want to derive the projection matrix that consists of both extrinsic camera calibration parameters (what are those?) and the intrinsic calibration matrix (again, what is that?)
Given: a set of image-scene point correspondences
Output: the projection matrix
It sounds like we have solved a similar problem before!!
Remember the process of homography estimation
What is the comparison?
In homography estimation we solved a matrix using a correspondence
Here we have to solve a matrix using a correspondence
Remember that we are using homogeneous coordinates
Steps?
Initialization using linear estimation
Optimization using maximum likelihood estimation

## Slide 19
11.3.3 Camera calibration from a known scene
We want to derive the projection matrix that consists of both extrinsic camera calibration parameters (what are those?) and the intrinsic calibration matrix (again, what is that?)
Given: a set of image-scene point correspondences
Output: the projection matrix
It sounds like we have solved a similar problem before!!
Remember the process of homography estimation
What is the comparison?
In homography estimation we solved a matrix using a correspondence
Here we have to solve a matrix using a correspondence
Remember that we are using homogeneous coordinates
Steps?
Step 1 Initialization using linear estimation
Step 2 Optimization using maximum likelihood estimation

## Slide 20
Step 1 Initialization using linear estimation
We want to derive the projection matrix that consists of both extrinsic camera calibration parameters (what are those?) and the intrinsic calibration matrix (again, what is that?)
Multiply the equation by to get (Remember how is formed?)
Rearrange the expression to get where
Integrate all correspondences into a single system of linear equation
Compute eigenvectors and eigenvalues of
Find along the eigenvector associated with the smallest eigenvalue subject to

## Slide 21
Step 2 Maximum Likelihood Estimation
Cost function :