## Slide 1: CFD Pre-Lab 1 Simulation of Laminar Pipe Flow Seong Mo Yeon, Timur Dogan, and Michael Conger 10/07/2015
Notes: Introduce yourself
Introduce Lab – Simulation of Laminar Pipe Flow in smooth pipe

## Slide 2: Outline
Overview of Pipe Flow
CFD Process
ANSYS Workbench
ANSYS Design Modeler (Geometry)
ANSYS Mesh
ANSYS Fluent
  Physics (Setup)
  Solution
  Results

## Slide 3: Overview of Pipe Flow
Simulation of laminar pipe flow will be conducted for this lab
Axial velocity profile, centerline velocity, centerline pressure, and wall shear stress will be analyzed
Computational fluid dynamics (CFD) results for friction factor and velocity profile will be compared to analytical fluid dynamics (AFD)
This lab will cover concept of laminar vs. turbulent flow and developing length for pipe flows
Flow visualization between two parallel plates
(starts at 14:25)
Notes: Questions:
What is the velocity at the wall?
Talking Points:
Simulating laminar pipe flow
Comparing CFD results to AFD solutions
Look at the developing profile
  Uniform inlet to quadratic
  Linear pressure drop in fully developed flow
  Developing length

## Slide 4: Overview of Pipe Flow
Flow in pipe with Reynolds (Re) number
  where U inflow velocity, D diameter of pipe, kinematic viscosity
  Laminar : Re < 2300
  Turbulent : Re > 2300
Differences between laminar and turbulent flow
  (mean) Velocity profile
  Pressure drop
  Developing length
  Wall shear stress and friction factor
  Note: Refer to Chapter 8 of your book for more details
Flow visualization of transition from laminar to turbulent flow
Notes: Talking Points:
Laminar flow is viscous dominated
  Low Re #
Turbulent flow is inertial dominated
  High Re #

## Slide 5: CFD Process
The overall procedure for simulation of pipe flow is shown on chart below
Although we will be making the mesh before we define the physics you have to know the physics to design appropriate mesh.
Geometry
Physics
Mesh
Solution
Results
Pipe (ANSYS Design Modeler)
Structure (ANSYS Mesh)
Uniform (ANSYS Mesh)
General (ANSYS Fluent - Setup)
Model (ANSYS Fluent - Setup)
Boundary Conditions (ANSYS Fluent -Setup)
Reference Values (ANSYS Fluent - Setup)
Laminar
Solution Methods (ANSYS Fluent - Solution)
Monitors (ANSYS Fluent - Solution)
Solution Initialization (ANSYS Fluent -Solution)
Plots (ANSYS Fluent- Results)
Graphics and Animations (ANSYS Fluent- Results)
Notes: Talking Points:
Physics must be known to properly construct mesh/grid
  Example: must know if flow is turbulent to determine grid refinement for B.L.
    Need many grid points to resolve large velocity grads noticed in turbulent B.L.
In ANSYS mesh comes before physics

## Slide 6: ANSYS Workbench (Overview)
Design your simulation using ANSYS Workbench
ANSYS Design Modeler
(Geometry)
ANSYS Mesh
(Mesh)
ANSYS Fluent
(Physics, Solution and Results)
Notes: Talking Points:
ANSYS Workbench Project Schematic screen
Modular interface
Geometry-> Mesh-> Physics-> Solution->Results

## Slide 7: ANSYS Design Modeler (Geometry)
Parameter | Value
Radius of pipe, R | 0.02619 m
Diameter of pipe, D | 0.05238 m
Length of pipe, L | 7.62 m
L
R
D
Inlet
Outlet
Wall
Center
Symmetric property of the flow is used to create 2D representation of the 3D pipe flow
Flow
Notes: Talking Points:
In CFD it is best to simplify problem for efficiency
Pipe can be simplified into 2D rectangle axisymmetric about centerline

## Slide 8
Create uniform grid distribution
ANSYS Mesh
Notes: Talking Points:
CFD is discretizing the fluid flow and solving N.S. eqns numerically at each grid point
Discretize geometry by splitting sides
Can get information at any discretized point

## Slide 9: ANSYS Fluent
Using ANSYS fluent define physics of the flow, solve CFD simulation and analyze results
Physics (Setup)
Solution
Results
Notes: Talking Points:
User interface of Fluent
Physics (Setup)
Solution
  Numerical methods setup
Results

## Slide 10: Physics
Laminar flow
Air properties
Boundary Conditions (BC)
  No-slip: velocities are zero (), pressure gradient () is zero
  Symmetric: radial velocity is zero (), gradients of axial velocity and pressure are zero (, )
  Inlet velocity: uniform constant velocity ()
  Outlet: (gauge) pressure is imposed to the boundary (, )
Inlet – Velocity inlet BC
Outlet – Pressure outlet BC
Wall – No slip BC
Center – Axisymmetric BC
Flow
ANSYS Fluent
Zero slop at center or
r
x
Notes: Talking Points:
No slip wall
Symmetric about axis for axial velocity and pressure
Uniform inlet velocity
Outlet pressure

## Slide 11
A limiting behavior in the solution of the equations
Represented by the history of residuals or errors made by previous iterative solutions.
A converged solution is not necessarily an accurate one due to iteration number, domain size, mesh resolution and numerical schemes
Continuity, momentum equation have their own residual histories.
ANSYS Fluent
Solution
Notes: Talking Points:
Residuals are relative errors, taking the difference between the previous solution and current solution
Just because residuals go to zero does not mean solution is perfectly accurate
  May be converging to the wrong solution
    Dependent on many factors such as turbulence modeling

## Slide 12
Developed length is distance from entrance to a point where flow is fully developed.
Fully developed flow does not change velocity profile or velocity gradient in axial direction is zero.
Pressure drops linearly.
Axial velocity or skin friction distribution along axis can be used to determine the length.
Developing
region
Developed region
ANSYS Fluent
Results
Notes: Questions:
Can anyone explain what fully developed flow is?
Why is friction coefficient constant in fully developed
Talking Points:
Explain developing length
Linear pressure drop in fully developed

## Slide 13
ANSYS Fluent
Results
Flow can be visualized in detail using CFD
Notes: Questions:
What happens to radial velocity in developed region?
Talking Points:
Shows contours of axial velocity
Vectors of axial velocity
CFD allows you to find fluid properties at any point in the fluid domain

## Slide 14: Questions?
Bring your Data Reduction Sheet for the CFD Labs
Deadline for CFD Lab report is two weeks after your CFD lab (not pre-lab)
Use lab drop-box when turning in your lab reports
Come to the office hours for help