## Slide 1: CFD Pre-Lab 2 Simulation of Turbulent Flow around an Airfoil Seong Mo Yeon, and Timur Dogan 11/12/2013

## Slide 2: Outline
Overview of Flow Around Airfoil
CFD Process
Workbench Geometry
Physics
Mesh
Solution
Results

## Slide 3: Overview of Flow Around Airfoil
Simulation of flow around airfoil will be conducted for this lab
Computational fluid dynamics (CFD) results for drag and lift coefficients, coefficient of pressure around the airfoil will be compared to experimental fluid dynamics (EFD)
This lab will cover concept of boundary layer and flow separation
Flow visualization around airfoil
(starts at 5:34)

## Slide 4: Overview of Flow Around Airfoil
Boundary Layer
  Defined by Ludwig Prandtl
  Generated by viscosity near wall
  Cause of lift and drag forces
  Inviscid vs. viscous flow
  Flow separation
  Note: Refer to Chapter 9 of your book for more details
Flow visualization of boundary layer
(Start at 3:21)

## Slide 5: CFD Process
The overall procedure for simulation of flow around airfoil is shown on chart below
Although we will be making the mesh before we define the physics you have to know the physics to design appropriate mesh.
Geometry
Physics
Mesh
Solution
Results
Airfoil (ANSYS Design Modeler)
Structured (ANSYS Mesh)
Non-uniform (ANSYS Mesh)
General (ANSYS Fluent - Setup)
Model (ANSYS Fluent - Setup)
Boundary Conditions (ANSYS Fluent -Setup)
Reference Values (ANSYS Fluent - Setup)
Turbulent
Solution Methods (ANSYS Fluent - Solution)
Monitors (ANSYS Fluent - Solution)
Solution Initialization (ANSYS Fluent -Solution)
Plots (ANSYS Fluent- Results)
Graphics and Animations (ANSYS Fluent- Results)
C-Domain (ANSYS Design Modeler)
O-Domain (ANSYS Design Modeler)
Solution Initialization
(ANSYS Fluent - Solution)
Solution Controls (ANSYS Fluent - Solution)
Run Calculation
(ANSYS Fluent - Solution)

## Slide 6: Geometry
Parameter | Value
Chord length, c | 0.3048 m
Radius of domain, Rc | 12.0 m
Angle of attack, α | 0, 16
Import Clark-Y airfoil geometry
Split O-type domain into four pieces

## Slide 7
Inviscid and viscous models
Air properties based on experimental temperature measurements
Boundary Conditions (BC)
  No-slip: velocities are zero (), pressure gradient () is zero
  Inlet velocity: extracted from experimental data
  Outlet: (gauge) pressure is imposed to the boundary ()
Inlet – Velocity inlet BC
Outlet – Pressure outlet BC
Wall – No slip BC
Physics

## Slide 8
Mesh
Fine mesh at the boundary layer region to resolve large velocity gradients

## Slide 9: Solution
If you have problems with solution convergence reduce Under-Relaxation Factors. This issue is more likely to occur for large angle of attack cases.
Also you may need to increase the number of iterations

## Slide 10: Results
Chart: Coefficent of Lift (Cl) Distribution
| 0 | 4 | 8 | 12 | 16
Benchmark Data | 0.184 | 0.386 | 0.64 | 0.845 | 1.038
Pressure Distribution Measurement | 0.14775 | 0.98229
Load Cell Measurement | 0.14913 | 0.9776
CFD | 0.31933 | 1.0894
Chart: Coefficent of Drag (Cd) Distribution
| 0 | 4 | 8 | 12 | 16
Benchmark Data | 0.017 | 0.0301 | 0.0425 | 0.0642 | 0.109
Wake Velocity Profile Pitot | 0.12995
Load Cell Measurement | 0.014991 | 0.10417
Wake Velocity Profile Hot-wire | 0.19721
CFD | 0.021631 | 0.25937
Chart: Coefficent of Pressure (Cp ) Distribution at 0 AOA
| 0 | 1.25 | 2.5 | 5 | 7.5 | 10 | 15 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 90 | 80 | 70 | 60 | 50 | 40 | 30 | 20 | 15 | 10 | 7.5 | 5 | 2.5 | 1.25
Benchmark Data | 0.9879 | 0.87275 | 0.39262 | -0.11572 | -0.34115 | -0.45695 | -0.57559 | -0.66089 | -0.65602 | -0.6282 | -0.57327 | -0.49744 | -0.40916 | -0.30144 | -0.098318 | 0 | 0.046946 | -0.05244 | -0.07802 | -0.1303 | -0.11165 | -0.19364 | -0.23189 | -0.30989 | -0.33718 | -0.82684 | -0.93713 | -1.1188 | -1.3905 | -1.4784
Experimental-2013 | 0.7812 | 0.65696 | 0.28691 | -0.10742 | -0.29218 | -0.38378 | -0.46572 | -0.51752 | -0.51692 | -0.53112 | -0.49331 | -0.42692 | -0.3661 | -0.24688 | -0.087994 | 0 | 0.011353 | -0.050587 | -0.080591 | -0.10612 | -0.12649 | -0.15488 | -0.20482 | -0.2677 | -0.30445 | -0.6802 | -0.75038 | -0.90487 | -1.1274 | -1.1993
Experimental-2012 | 1.0012 | 0.93881 | 0.50718 | 0.047771 | -0.16439 | -0.28757 | -0.39747 | -0.46191 | -0.47683 | -0.44538 | -0.40957 | -0.33066 | -0.26565 | -0.21805 | 0.015108 | 0 | 0.12252 | 0.049338 | 0.01423 | -0.010254 | -0.040161 | -0.06886 | -0.13951 | -0.20041 | -0.24217 | -0.76022 | -0.81384 | -0.95607 | -1.2232 | -1.3722 | 0 | -0.0047966 | 1.04
experimental-2010 | 0.92146 | 0.87011 | 0.40445 | -0.10497 | -0.35682 | -0.49619 | -0.61401 | -0.69363 | -0.70588 | -0.67198 | -0.63468 | -0.55958 | -0.48509 | -0.36112 | -0.14643 | 0 | -0.026956 | -0.10538 | -0.14432 | -0.17979 | -0.20752 | -0.25024 | -0.31941 | -0.41675 | -0.47413 | -1.0559 | -1.1055 | -1.2929 | -1.545 | -1.7521 | 0 | 0.74534 | 1.0483
Chart: Coefficent of Pressure (Cp ) Distribution at 16 AOA
| 0 | 1.25 | 2.5 | 5 | 7.5 | 10 | 15 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 90 | 80 | 70 | 60 | 50 | 40 | 30 | 20 | 15 | 10 | 7.5 | 5 | 2.5 | 1.25
Benchmark Data | -0.78513 | -1.9842 | -2.2082 | -2.2091 | -2.0687 | -1.8836 | -1.6512 | -1.5204 | -1.0735 | -0.90726 | -0.75471 | -0.58686 | -0.41799 | -0.26672 | -0.11956 | 0.017092 | 0.022818 | 0.0084607 | 0.018203 | 0.035466 | 0.067258 | 0.10153 | 0.14075 | 0.20357 | 0.23647 | 0.27595 | 0.36022 | 0.4867 | 0.66215 | 0.92879
Experimental-2013 | -1.0407 | -2.079 | -2.2068 | -2.1553 | -1.9756 | -1.7956 | -1.5814 | -1.4491 | -0.99088 | -0.81033 | -0.67357 | -0.4864 | -0.33898 | -0.18745 | -0.056788 | 0 | 0.088208 | 0.10255 | 0.12082 | 0.13848 | 0.16837 | 0.197 | 0.23489 | 0.29129 | 0.3331 | 0.36934 | 0.45014 | 0.56751 | 0.70623 | 0.89801
Experimental-2010 | -0.74373 | -1.9366 | -2.1394 | -2.1264 | -1.967 | -1.819 | -1.5951 | -1.4675 | -1.0197 | -0.82208 | -0.66768 | -0.50561 | -0.34883 | -0.20626 | -0.062854 | 0 | 0.089281 | 0.079249 | 0.091889 | 0.10863 | 0.13627 | 0.16915 | 0.20257 | 0.26008 | 0.29433 | 0.31923 | 0.40004 | 0.53177 | 0.71142 | 0.948 | 0 | 0.016067 | 0.90048
experimental-2012 | -0.77838 | -1.8336 | -2.0123 | -2.0416 | -1.9243 | -1.7801 | -1.5669 | -1.44 | -1.0495 | -0.90082 | -0.77639 | -0.60222 | -0.42013 | -0.26677 | -0.13563 | 0 | 0.003821 | -0.010555 | 0.0023286 | 0.016461 | 0.039831 | 0.064767 | 0.094166 | 0.14247 | 0.17261 | 0.20438 | 0.26968 | 0.3764 | 0.53509 | 0.76929 | 0 | 0.67095 | 0.2274

## Slide 11: Possible Sources of Error
Inaccurate measurements by load cell 1 was observed.
The voltage for load cell 1 was significantly larger than the voltage for load cell 2.
Accurate results for CD, compared to benchmark data, were achieved using load cell 2 data.
Some students used incorrect directions for lift and drag, Y-direction indicates drag and z-direction indicates lift.

## Slide 12: Load Cell Error Fix
If you are experiencing large errors when comparing CFD to EFD for CD, you will need to recalculate CD.
aoa 0 | CL | CD | % Diff CL | % Diff CD
Benchmark (U=15m/s) | 0.184 | 0.017 | - | -
EFD (15.6 m/s) | 0.1585 | 0.0178 | 14% | 5%
EFD with incorrect load cell measurement (15.6 m/s) | 0.1585 | 0.0506 | 14% | 198%

## Slide 13: Load Cell Error Fix
Drag Lift
Load Cell 1
Drag Lift
Load Cell 2
Instead of inputting the summed voltage from the two load cells into the calibration curve for drag, input two times the voltage of load cell 2.

## Slide 14
Pressure distribution around airfoil
Velocity vectors near wall and boundary layer development
Stream lines around airfoil
Results