## Slide 1: CFD Pre-Lab 1 Simulation of Laminar Pipe Flow Seong Mo Yean, and Timur Dogan 10/14/2013

## Slide 2: Outline
Overview of Pipe Flow
CFD Process
ANSYS Workbench
ANSYS Design Modeler (Geometry)
ANSYS Mesh
ANSYS Fluent
  Physics (Setup)
  Solution
  Results

## Slide 3: Overview of Pipe Flow
Simulation of laminar pipe flow will be conducted for this lab
Axial velocity profile, centerline velocity, centerline pressure, and wall shear stress will be analyzed
Computational fluid dynamics (CFD) results for friction factor and velocity profile will be compared to analytical fluid dynamics (AFD)
This lab will cover concept of laminar vs. turbulent flow and developing length for pipe flows
Flow visualization between two parallel plates
(starts at 14:25)

## Slide 4: Overview of Pipe Flow
Flow in pipe with Reynolds(Re) number
  where U inflow velocity, D diameter of pipe, kinetic viscosity
  Laminar : Re < 2300
  Turbulent : Re > 2300
Differences between laminar and turbulent flow
  (mean) Velocity profile
  Pressure drop
  Developing length
  Wall shear stress and friction factor
  Note: Refer to Chapter 8 of your book for more details
Flow visualization of transition from laminar to turbulent flow

## Slide 5: CFD Process
The overall procedure for simulation of pipe flow is shown on chart below
Although we will be making the mesh before we define the physics you have to know the physics to design appropriate mesh.
Geometry
Physics
Mesh
Solution
Results
Pipe (ANSYS Design Modeler)
Structure (ANSYS Mesh)
Uniform (ANSYS Mesh)
General (ANSYS Fluent - Setup)
Model (ANSYS Fluent - Setup)
Boundary Conditions (ANSYS Fluent -Setup)
Reference Values (ANSYS Fluent - Setup)
Laminar
Solution Methods (ANSYS Fluent - Solution)
Monitors (ANSYS Fluent - Solution)
Solution Initialization (ANSYS Fluent -Solution)
Plots (ANSYS Fluent- Results)
Graphics and Animations (ANSYS Fluent- Results)

## Slide 6: ANSYS Workbench (Overview)
Design your simulation using ANSYS Workbench
ANSYS Design Modeler
(Geometry)
ANSYS Mesh
(Mesh)
ANSYS Fluent
(Physics, Solution and Results)

## Slide 7: ANSYS Design Modeler (Geometry)
Parameter | Value
Radius of pipe, R | 0.02619 m
Diameter of pipe, D | 0.05238 m
Length of pipe, L | 7.62 m
L
R
D
Inlet
Outlet
Wall
Center
Symmetric property of the flow is used to create 2D representation of the 3D pipe flow
Flow

## Slide 8
Create uniform grid distribution
ANSYS Mesh

## Slide 9: ANSYS Fluent
Using ANSYS fluent define physics of the flow, solve CFD simulation and analyze results
Physics (Setup)
Solution
Results

## Slide 10: Physics
Laminar flow
Air properties
Boundary Conditions (BC)
  No-slip: velocities are zero (), pressure gradient () is zero
  Symmetric: radial velocity is zero (), gradients of axial velocity and pressure are zero (, )
  Inlet velocity: uniform constant velocity ()
  Outlet: (gauge) pressure is imposed to the boundary (, )
Inlet – Velocity inlet BC
Outlet – Pressure outlet BC
Wall – No slip BC
Center – Axisymmetric BC
Flow
ANSYS Fluent
Zero slop at center or
r
x

## Slide 11
A limiting behavior in the solution of the equations
Represented by the history of residuals or errors made by previous iterative solutions.
A converged solution is not necessarily an accurate one due to iteration number, domain size, mesh resolution and numerical schemes
Continuity, momentum equation have their own residual histories.
ANSYS Fluent
Solution

## Slide 12
Developed length is distance from entrance to a point where flow is fully developed.
Fully developed flow does not change velocity profile or velocity gradient in axial direction is zero.
Pressure drops linearly.
Axial velocity or skin friction distribution along axis can be used to determine the length.
Developing
region
Developed region
ANSYS Fluent
Results

## Slide 13
ANSYS Fluent
Results
Flow can be visualized in detail using CFD

## Slide 14: Questions?
Bring your Data Reduction Sheet for the CFD Labs
Deadline for CFD Lab report is two weeks after your CFD lab (not pre-lab)
Use lab drop-box when turning in your lab reports
Come to the office hours for help